## Slide 1: N-detect TDF ATPG And Compression
Group : 13
Group Members:
B08505049 劉旻鑫
B08505039 林楷崴
R11943113 葉冠宏

## Slide 2: EXPERIMENTAL RESULT PROPOSED METHODS PROBLEM DESCRIPTION 01 02 TABLE OF CONTENTS 03
TEST LENGTH COMPARING
SCOAP
DTC
STC

## Slide 3: EXPERIMENTAL RESULT PROPOSED METHODS PROBLEM DESCRIPTION 01 02 TABLE OF CONTENTS 03
TEST LENGTH COMPARING
SCOAP
DTC
STC

## Slide 4: PROBLEM DESCRIPTION
Given sample circuit netlists, our goal is to generate a N-detect TDF ATPG in LOS mode.
In N-detect fault simulation, a fault will be dropped only when it is detected more than N times.
However, it leads to increased test cost. Hence, we should apply test compression techniques, including STC and DTC.

## Slide 5: EXPERIMENTAL RESULT PROPOSED METHODS PROBLEM DESCRIPTION 01 02 TABLE OF CONTENTS 03
TEST LENGTH COMPARING
SCOAP
DTC
STC

## Slide 6: 0VERALL ATPG FLOW STC DTC
TDF ATPG with DTC
STC#1
STC#2
Compute SCOAP
ATPG DONE

## Slide 7: DYNAMIC TEST COMPRESSTION
Choose primary fault by order
First find V2 to detect certain fault
Check if it can be activated by V1
Randomly choose secondary fault
At the end, we randomly fill unknown bits

## Slide 8: DYNAMIC TEST COMPRESSTION FLOW
NO
YES
NO
YES
Select a secondary fault
Test pattern generation
Select a primary fault
Test pattern generation
More secondary faults and enough unknown bits ?
Fill unknown bits
TDF fault simulation
All faults are dropped or tried ?
ATPG with DTC done

## Slide 9: STATIC TEST COMPRESSTION
STC#1
                First, do reverse order simulation to drop faults
        STC#2
            Second, reorder the test patterns according to the detected fault number
        Then, do fault simulation in the order to drop faults

## Slide 10: STATIC TEST COMPRESSTION FLOW
Reverse Pattern Order
TDF simulate one pattern
Remove this pattern
Detect any fault ?
Any pattern remains ?
Reverse STC Done
NO
NO
Yes
Yes
Sort patterns based on detected fault number
TDF simulate one pattern
Detect any fault ?
Remove this pattern
Any pattern remains ?
STC Done
NO
YES
NO
YES

## Slide 11: EXPERIMENTAL RESULT PROPOSED METHODS PROBLEM DESCRIPTION 01 02 TABLE OF CONTENTS 03
TEST LENGTH COMPARING
SCOAP
DTC
STC

## Slide 12: Test Length Compare with PA3 w/ compression
Test Length (PA3) | Fault Coverage
20 | 0.27
66 | 64.94
65 | 37.64
62 | 21.75
135 | 71.6
98 | 14.44
42 | 95.14
288 | 89.54
Circuit Number | Test Length (N = 1) | Fault Coverage
c432 | 23 | 11.62
c499 | 82 | 94.77
c880 | 68 | 49.76
c1355 | 65 | 38.41
c2670 | 135 | 92.81
c3540 | 89 | 22.92
c6288 | 81 | 97.27
c7552 | 249 | 97.93

## Slide 13: Test Length Difference between N=1 and N=8 w/o compression
Circuit Number | Test Length (N = 8) | Fault Coverage | Run Time
c432 | 179 | 11.62 | 0.1
c499 | 750 | 91.17 | 0.7
c880 | 686 | 49.19 | 0.9
c1355 | 501 | 32.94 | 2.4
c2670 | 1481 | 91.73 | 2.8
c3540 | 896 | 22.88 | 11.5
c6288 | 303 | 96.82 | 9.8
c7552 | 3007 | 97.58 | 12.9
Circuit Number | Test Length (N = 1) | Fault Coverage | Run Time
c432 | 27 | 11.62 | 0.1
c499 | 118 | 94.31 | 0.42
c880 | 111 | 49.24 | 0.7
c1355 | 88 | 38.41 | 2.12
c2670 | 228 | 92.47 | 1.54
c3540 | 137 | 22.96 | 10.33
c6288 | 83 | 97.23 | 6.15
c7552 | 449 | 97.73 | 5.7

## Slide 14: Test Length Difference between N=1 and N=8
Chart: Test Length Growth from N=1 ~ 8 (before DTC+STC)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
c432 | 27 | 49 | 74 | 93 | 116 | 143 | 162 | 179
c499 | 118 | 219 | 317 | 415 | 500 | 580 | 660 | 750
c880 | 111 | 182 | 275 | 349 | 433 | 520 | 588 | 686
c1355 | 88 | 159 | 225 | 279 | 340 | 393 | 448 | 501
c2670 | 228 | 402 | 592 | 756 | 967 | 1118 | 1280 | 1481
c3540 | 137 | 258 | 381 | 468 | 603 | 704 | 791 | 896
c6288 | 83 | 119 | 162 | 190 | 219 | 254 | 265 | 303
c7552 | 449 | 828 | 1206 | 1569 | 1894 | 2287 | 2701 | 3007
Chart: Test Length Growth from N=1 ~ 8 (after DTC+STC)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
c432 | 23 | 47 | 69 | 87 | 114 | 131 | 173 | 173
c499 | 82 | 144 | 213 | 287 | 371 | 401 | 481 | 565
c880 | 68 | 118 | 173 | 212 | 259 | 308 | 377 | 412
c1355 | 65 | 122 | 191 | 250 | 300 | 348 | 392 | 438
c2670 | 135 | 241 | 366 | 466 | 565 | 675 | 772 | 875
c3540 | 89 | 161 | 229 | 307 | 364 | 472 | 506 | 600
c6288 | 81 | 149 | 180 | 214 | 265 | 294 | 333 | 369
c7552 | 249 | 461 | 668 | 904 | 1115 | 1285 | 1532 | 1670

## Slide 15: Test Length Difference between Compression N = 8
Circuit Number | Test Length w/ comp | Fault Coverage | Run Time
c432 | 173 | 11.62 | 0.2
c499 | 565 | 91.13 | 0.9
c880 | 412 | 49.24 | 1.4
c1355 | 438 | 32.94 | 2.8
c2670 | 875 | 92.38 | 6.3
c3540 | 600 | 22.91 | 14.5
c6288 | 369 | 96.14 | 21.2
c7552 | 1670 | 97.83 | 26.7
Circuit Number | Test Length w/o comp | Fault Coverage | Run Time
c432 | 179 | 11.62 | 0.1
c499 | 750 | 91.17 | 0.7
c880 | 686 | 49.19 | 0.9
c1355 | 501 | 32.94 | 2.4
c2670 | 1481 | 91.73 | 2.8
c3540 | 896 | 22.88 | 11.5
c6288 | 303 | 96.82 | 9.8
c7552 | 3007 | 97.58 | 12.9

## Slide 16: Test Length Difference between Compression N = 8
Circuit Number | Test Length w/o comp | Test Length w/ comp | Reduction Rate (%)
c432 | 179 | 173 | 3.35
c499 | 750 | 565 | 24.67
c880 | 686 | 412 | 39.94
c1355 | 501 | 438 | 12.57
c2670 | 1481 | 875 | 40.92
c3540 | 896 | 600 | 33.04
c6288 | 303 | 369 | -21.78
c7552 | 3007 | 1670 | 44.46
Chart: c7552, N=8, Test Length Comparison
w/o compression | 3007
DTC_only | 2041
DTC+STC_1 | 1789
DTC+STC_1+STC_2 | 1670

## Slide 17: Possible Improvements
Reorder the fault list before ATPG
Fill unknown bits more wisely
Choose secondary fault more wisely

## Slide 18: Contribution
劉旻鑫: DTC、Simulation
林楷崴: Utility Functions、PPT、Report
葉冠宏: STC

## Slide 19: Reference
Goel, "An Implicit Enumeration Algorithm to Generate Tests for Combinational Logic Circuits," in IEEE Transactions on Computers, vol. C-30, no. 3, pp. 215-222, March 1981, doi: 10.1109/TC.1981.1675757.
[Hamzaoglu 98] I.Hamzaoglu, J.Patel, “Test set compaction algorithms for combinational circuits”, ICCAD 1998
D. Xiang, W. Sui, B. Yin and K. -T. Cheng, "Compact Test Generation With an Influence Input Measure for Launch-On-Capture Transition Fault Testing," in IEEE Transactions on Very Large Scale Integration (VLSI) Systems, vol. 22, no. 9, pp. 1968-1979, Sept. 2014, doi: 10.1109/TVLSI.2013.2280170.
B. Benware et al., "Impact of multiple-detect test patterns on product quality," International Test Conference, 2003. Proceedings. ITC 2003., Charlotte, NC, USA, 2003, pp. 1031-1040, doi: 10.1109/TEST.2003.1271091.

## Slide 20: Thank You 13
For Your Attention